## Slide 1
FORMULA STUDENT DRIVERLESS
Full-Stack Autonomous Systems Architecture
Perception, State Estimation, FastSLAM 2.0, MPC Control & Testing Infrastructure
Notes: Good morning everyone. In this presentation, I will walk you through the end-to-end autonomous pipeline for a Formula Student Driverless vehicle. We will cover Perception—combining LiDAR and Camera data, State Estimation via Extended Kalman Filtering, Mapping using FastSLAM 2.0, Path Planning with Delaunay Triangulation, and Model Predictive Control for high-speed tracking. Finally, I will detail our simulation and testing workflows, as well as an explicit disclosure on how AI tools were leveraged to assist in preparing this presentation.

## Slide 2
FORMULA STUDENT DRIVERLESS
Perception: LiDAR & Camera Fusion
LiDAR Pipeline
• Ground Filtering: RANSAC/grid segmentation isolates drivable surface.
• Motion Deskewing: High-speed frame motion distorts point clouds. High-freq IMU/odometry transforms points back to frame start time.
• Clustering & Reconstruction: DBSCAN/Euclidean extraction groups sparse cone returns; shape-fitting extracts 3D centroids.
• Color via Intensity: Reflective tape on cones produces high intensity return peaks for color classification.
Camera Pipeline
• CNN Keypoint Detection: Predicts 2D bounding boxes & cone keypoints (top, base corners).
• Mono vs. Stereo: Monocular assumes ground homography/cone size (vulnerable to pitch). Stereo directly computes depth Z = (f * B) / d.
• Epipolar Matching: Restricts stereo keypoint searches along 1D horizontal scanlines.
• PnP Projection: Converts 2D pixel keypoints to precise 3D camera-frame coordinates.
Fusion & Redundancy
• Sensor Redundancy: LiDAR excels at 3D geometry & long-range depth but lacks dense color. Cameras provide rich semantic color but suffer in poor lighting.
• Cross-Modal Fusion: Merges LiDAR spatial accuracy with Camera color classification.
• Fail-safe Perception: Ensures zero single-point-of-failure under bright glare or rain.
Notes: Moving to Perception. The LiDAR pipeline filters ground points and compensates for motion distortion—or deskewing. Because a LiDAR scan takes ~100ms, vehicle motion distorts the frame unless points are transformed using IMU odometry. Cones are clustered and colored based on retroreflective intensity peaks. On the Camera side, CNNs detect cone keypoints. While monocular depth relies on size assumptions, stereo camera depth uses disparity matching across horizontal epipolar lines. Combining both sensors provides vital redundancy: LiDAR handles accurate 3D spatial positioning, while cameras provide reliable color semantics.

## Slide 3
FORMULA STUDENT DRIVERLESS
State Estimation & Velocity Tracking
EKF & Velocity Estimation
• High-Frequency Feedback: Controllers require real-time estimates (>100Hz) of longitudinal velocity (vx), lateral velocity (vy), and yaw rate (wz).
• Extended Kalman Filter (EKF): Fuses kinematic/dynamic vehicle models with multi-sensor updates.
• Prediction Step: Propagates vehicle state forward using IMU angular rates & linear accelerations.
• Update Step: Corrects state predictions using wheel encoders, optical speed sensors, and SLAM position estimates.
Sensor Redundancy & Slip
• Why Single Sensors Fail: Individual sensors cannot be trusted in high-speed racing conditions.
• Wheel Encoders: Suffer from severe wheel slip under acceleration/lockup under braking.
• IMU Drift: Uncorrected integration of accelerometer bias leads to massive position drift.
• Outliers vs. Drift: Mahalanobis distance gating filters measurement outliers, while non-integrating global updates eliminate drift.
Notes: Next is State Estimation. High-performance controllers need stable velocity estimates at over 100 Hz. We run an Extended Kalman Filter fusing a dynamic vehicle model with sensor updates. Why can't we trust individual sensors? Wheel encoders slip during aggressive acceleration and braking, and raw IMU integration suffers from unconstrained drift. By fusing encoders, IMUs, and optical speed sensors—and filtering outliers via Mahalanobis distance gating—our EKF maintains an accurate estimate of vehicle motion even at tire traction limits.

## Slide 4
FORMULA STUDENT DRIVERLESS
SLAM & Mapping Infrastructure
FastSLAM 2.0 Architecture
• Unknown Track Problem: The vehicle enters an unknown track and must simultaneously build a landmark map (cone locations) and localize itself.
• Data Association Challenge: Corresponds newly detected cones to mapped landmarks. Solved using Mahalanobis distance and JCBB (Joint Compatibility Branch & Bound).
• FastSLAM 2.0 Engine: Uses a Rao-Blackwellized Particle Filter. Each particle holds a vehicle trajectory hypothesis and independent landmark EKFs.
• Proposal Distribution: FastSLAM 2.0 incorporates the latest sensor observation into particle proposal, drastically reducing required particle count.
• Lap Closure Transition: Detects start line re-entry, freezes map building, and transitions to global path optimization for maximum speed.
Notes: For Mapping, we face the unknown track problem solved by FastSLAM 2.0. The main difficulty in SLAM is data association: matching observed cones to previously mapped landmarks. FastSLAM 2.0 uses a Rao-Blackwellized Particle Filter where each particle maintains the vehicle trajectory and independent EKFs for landmark locations. Unlike FastSLAM 1.0, version 2.0 incorporates the latest observation directly into the particle proposal step, keeping particle counts low and real-time capable. Once Lap Closure is detected at the start line, map building freezes, transitioning the system to global trajectory pursuit.

## Slide 5
FORMULA STUDENT DRIVERLESS
Path Planning & Vehicle Control
Path Planning & Racing Line
• Delaunay Triangulation: Connects yellow (left) and blue (right) cones into a geometric mesh; removing same-color edges extracts the track centerline.
• Racing Line vs. Centerline: Centerline driving restricts speed. Racing lines optimize apex trajectory to maximize cornering radius (R).
• Curvature Acceleration: Minimizes lateral acceleration ay = (v^2) / R to allow higher cornering velocities.
• Cost Function: Scores candidate paths based on curvature smoothness, cone boundary clearance, and speed profile feasibility.
MPC & Bicycle Model Control
• Model Predictive Control (MPC): Solves online constrained optimization over a prediction horizon N.
• Actuator Constraints: Minimizes tracking error while respecting steering rate limits and acceleration bounds.
• Bicycle Model Dynamics: Models vehicle response using front/rear tire slip angles (alpha_f, alpha_r) and cornering stiffness (C_alpha).
• Real-Time Execution: Computes optimal steering & torque commands within tight 20ms control loops.
Notes: In Planning and Control, candidate paths are generated via Delaunay Triangulation across left and right cones. However, driving the track centerline is sub-optimal for racing. We optimize a global racing line to maximize the cornering radius R at the apex. Since lateral acceleration is ay = v squared over R, a larger radius allows higher cornering speeds. For Control, we use Model Predictive Control based on a Dynamic Bicycle Model incorporating tire slip angles. MPC solves an online optimization problem every 20 milliseconds, calculating optimal steering and motor torques while strictly adhering to actuator limits.

## Slide 6
FORMULA STUDENT DRIVERLESS
Testing Infrastructure & AI Disclosure
Simulation & Testing (ATS)
• Simulation Utility: SIL and HIL simulation pipelines validate perception, SLAM, and control algorithms without risking physical car crashes.
• Automated Testing System (ATS): CI/CD regression framework that replays sensor rosbags and simulated track edge-cases on every pull request.
• Telemetry & Analytics: Comprehensive logging of CAN bus, sensor pipelines, and controller outputs for offline lag & stability analysis.
AI Usage Disclosure
• AI Role & Scope: AI tools were used as a thought partner, code generator, and verification assistant.
• Architectural Mapping: Assisted in structuring technical guidelines into clear 5-7 minute presentation narratives.
• Code & Slide Generation: Generated python-pptx scripts to build slide layouts and formatted markdown bullet points.
• Mathematical Verification: Used to cross-check coordinate transformations, EKF formulations, and bicycle model kinematics.
Notes: Finally, Testing and AI Methodology. Before running the real vehicle, all algorithms undergo Software and Hardware-in-the-Loop simulation. Our Automated Testing System replays rosbags via CI/CD to catch performance regressions. Regarding AI Usage: AI was leveraged as a collaborative thought partner throughout this process—specifically for structuring the technical slide narrative to fit the 5-7 minute window, generating the underlying python-pptx presentation code, and verifying mathematical derivations for coordinate frames and state estimation formulas. Thank you, and I am now ready for your questions!